## Slide 1: CDR Presentation
Apex

## Slide 2: Mission Requirements
Apex has designed a rocket engine to meet the following criteria:
  Hybrid engine utilizing liquid N2O oxidizer
  Produce between 75 and 150 lbs thrust
  Total impulse at least 500 lb-sec
  Able to throttle to 70% thrust in flight
  To apply our engineering knowledge to an unusual problem, alternative nozzle types were explored.
Notes: Difference between rocket engine and motor?

## Slide 3: Assembly
Bell Nozzle
  Height 36.56 in
  Width 4.3 in
  Dry Weight 11.16 lbs
  Wet Weight 13.45 lbs
Oxidizer
Tank
Plumbing &
Valves
Injector

## Slide 4: Oxidizer Tank
Apex

## Slide 5: Oxidizer Tank
Dimensions
  Height 10.8 in
  Diameter 3.21 in
Material 6061 T6 Aluminum
Weight
  Empty 2.62
  Full 4.91
Pressure
  Rated 3000 psi
  Operates 1000 psi
9
2x1

## Slide 6: Valves and plumbing
Apex

## Slide 7: Plumbing
Feed System Schematic
Custom Oxidizer Tank Manifold Fitting
Union: Male ½” pipe to ½” tube
½” Primary Line
45 Elbow: Male ½” pipe to ½” tube
90 Elbow: Male SAE 8 to Female ½” pipe
Electrical Proportionality Valve - Cartridge
Electrical Proportionality Valve – Coil
Electrical Proportionality Valve - Body
Union: Male SAE 8 to Male SAE 8
Quick Connect Stem
Vent Stem
1
From Oxidizer Tank
To Injector Manifold
3
6
7
8
5
4
2
9
10
11
3
4x2

## Slide 8: Throttling Valve
- NC Electronic Proportionality Valve
  Pros: Single Valve, Reduced Actuation Time, and uses only 1 actuator
  Hydraforce SP08-20
  Solenoid operated poppet cartridge valve
  6 Volts with Resistance of 2.46 Ohms
  Initial Current Draw of 2.44 Amps
Note: This plot uses Mineral Oil as its fluid
3
4x2

## Slide 9: Throttle Valve Controller
- Arduino Pro Mini
  Low voltage 3.3 V – Variable Input
  14 Digital I/O Pins with PWM
  16 KB of Flash Memory
  1 KB of SRAM
  512 bytes of EEPROM
  8 MHz Clock Speed
  Use Pulse Width Modulation to control throttling
  Activation of program once 5 V input voltage is applied
- Power
  6 NiMH Tenergy 1.2 Volt Battery @ 2500 mAh
  2C Rating
3
4x2

## Slide 10: Injector
Apex

## Slide 11: Injector
Outer Holes
  Diameter: 0.052in
  Angle: 75o from horizontal
Inner Holes
  Diameter: 0.026in
  Angle: 90o from horizontal
Impingement Point
  2in below lower injector face
3
4x1

## Slide 12: Injector
Flow without the top coin
Flow is highly dependant on position of injector coin relative to incoming flow
3
4x1

## Slide 13: Injector
Top coin channels flow so the flow is evenly distributed through the outer holes
3
4x1

## Slide 14: Combustion Chamber
Apex

## Slide 15
Fuel Selection & Grain Geometry
Ideal Fuel Properties
Fuel Choice: HTPB
(Hydroxyl-Terminated Polybutadiene)
Casted Fuel
Good Isp (at least 200 sec)
Low Combustion Temperature
Proven and Reliable fuel
Good Stability

## Slide 16
Fuel Properties
3.5 N2O : 1 HTPB
Chamber Temperature: 2400 K
(Allows for more material flexibility in the nozzle)
Isp: 203 s
Cf: 1.39
C*: 1434 m/s
ε: 3.25
Gamma: 1.31
Molar Mass: 21.95 g/mol

## Slide 17: Fuel Grain Cut-Away
Fuel Grain (HTPB)
Phenolic Liner (.08” thick)
Combustion Chamber
(.125” thick Aluminum)
|----1.83” ID-----|
3
3x1

## Slide 18
Mass Values
ṁp | .138 lb/s
ṁo | .482 lb/s
ṁf | .620 lb/s
mp | 0.55 lb
mp carried | .61 lb (11% extra)
mo | 1.94 lb
mo carried | 2.30 lb (19% extra)
Nicholas Oliviero

## Slide 19: Combustion Chamber Assembly
3
HTPB (8”)
Pre-Combustion
Chamber (2”)
Post-Combustion
Chamber (1.5”)
Phenolic Lining
Bulkheads/Flanges
4x2

## Slide 20: Bell Nozzle
Apex

## Slide 21: Bell Nozzle
Contour is a Rao cubic polynomial
Area Ratio: 3.35
Throat Area: 0.29
Exit Area: 0.98
Thrust Coeff.: 1.39
Exit Mach Number: 2.53
Throat to Exit Length: 1.25in
4
4x2

## Slide 22: Results and Comparison
Modeled with a 1:1 mixture of Nitrogen and Carbon Dioxide
Validated when compared to a 1-D approximation
4
4x2

## Slide 23: Aerospike Nozzle
Apex

## Slide 24: Aerospike
Centered Prandtl-Meyer all external expansion
More efficient over wide altitude range
Compensates for changes in atmospheric pressure
Apply engineering knowledge to an unusual and non-trivial problem
3
4x2

## Slide 25: Aerospike Structure
7 different pieces
Primarily built of graphite
Steel adding structural support
Steel incased in graphite to protect from flow
Graphite cowl to create throat area
Entire assembly interchangeable with Bell nozzle
3
4x2

## Slide 26: Flow Simulation
Performance evaluated at sea level
At right, Mach number plotted on computation mesh
Left: Mach streamlines generated
No major recirculation zones present
3
4x2

## Slide 27: Nozzle Interchangeability
Each nozzle built to be quickly swapped out
Outer cowl designed to hold both graphite nozzles

## Slide 28: Supporting Information
Apex

## Slide 29: O/F Ratio Selection

## Slide 30: Preliminary Design

## Slide 31: Aerospike Dimensions
All units in inches

## Slide 32: Technology Readiness Level
Matthias Breal
Technology Readiness Level | 
1 | Basic principles observed and reported
2 | Technology concept and/or application formulated
3 | Analytical and experimental critical function and/or characteristic proof of concept
4 | Component and/or breadboard validation in laboratory environment
5 | Component and/or breadboard validation in relevant environment
6 | System/subsystem model or prototype demonstration in a relevant environment
7 | System prototype demonstration in an operational environment
8 | Actual system completed and “flight qualified” through test and demonstration
9 | Actual system “flight proven” through successful mission operations
Section | TRL
Combustion Chamber | 3
Fuel Grain | 3
Tank | 9
Bell Nozzle | 4
Star Nozzle | 2
Valves | 3
Ignition system | 9
Injector | 3

## Slide 33: Risk Assessment
Section | Severity of Failure | Likelihood of Failure
Combustion Chamber | 4 | 2
Fuel Grain | 3 | 1
Tank | 2 | 1
Bell Nozzle | 4 | 2
Star | 4 | 2
Valves | 4 | 2
Ignition system | 4 | 3
Injector | 4 | 1
Matthias Breal
Severity of Failure | 
Mission Impact Level | Risk Level
1 | Minimal
2 | Minor
3 | Moderate
4 | Significant
5 | Severe
Likelihood of Failure | 
Mission Impact Level | Risk Level
1 | Negligible
2 | Unlikely
3 | Likely
4 | Highly Probably
5 | Near Certainty